## Slide 1
Sample UAV HS data classification
INSTITUTE OF GEOGRAPHY, FACULTY OF SCIENCE, PAVOL JOZEF ŠAFÁRIK UNIVERSITY IN KOŠICE, SLOVAKIA
Katarína ONAČILLOVÁ, Michal GALLAY, Ján ŠAŠAK
geografia.science.upjs.sk katarina.onacillova@upjs.sk
INTERNATIONAL REMOTE SENSING SUMMER SCHOOL , IV EDITION
Experiencing Remote Sensing on Sardinia inland site: Advanced summer school on instruments and methodology for a CAL/VAL site for Optical data SAN VERO MILIS | SARDINIA, italy | 21. - 25. JULY 2025

## Slide 2: Image classification
The process of sorting pixels into a certain number of classes based on their data values
Finding meaningful patterns in the data (spectral and spatial)
Simplify/refine the interpretation of the RS record
Corine Land Cover

## Slide 3: 2 approaches
Object-oriented (OBIA) (OBIA)
  It uses both spectral information and its spatial distribution

## Slide 4: 2 approaches
Pixel- based (per-pixel)
  It uses only spectral information
  It does not use spatial distribution and neighborhood relations
Types:
  Supervised classification
  Unsupervised classification
  Based on a different rule

## Slide 5: Unsupervised classification
The raw spectral data are grouped based on the statistical structure of the data only
Then the computer assigns each statistical cluster into the appropriate class (if possible)

## Slide 6: Supervised classification
The user defines homogeneous, representative samples, so-called training samples (areas) of different types of land cover
Based on the selected algorithm, the computer assigns the pixels to the visually closest class based on the training areas
Good knowledge of the classified area and good visual interpretation are ideal

## Slide 7: Supervised classification
Types:
Minimum Distance-to-Means – average DN values
Maximum Likelihood
  probability of class membership
Spectral Angle Mapper
  the minimum angle from the n-dimensional
spectral vector of the class

## Slide 8: CONTENT OF THIS PRACTICAL
1
Spectral signatures
2
Image classification
MULTISPEC

## Slide 9: INPUT HS DATA
Capture reflected electromagnetic energy in hundreds of contiguous narrow spectral bands
Combined with UAS:
  fast, flexible and non-destructive detection of subtle spectral features
CHM (Canopy Height Model)
+ I N P U T L S D ATA
AISA Kestrel 10
Push-broom camera, 4.75 kg
Spatial resolution: 1024 or 2048 pix.
Spectral range: 400 – 1000 nm
Max. number of spectral bands: 342

## Slide 10: MULTISPEC
I. SPECTRAL SIGNATURES

## Slide 11: STATE-OF-THE-ART
Spectral signatures and their interpretation
When EMR from the sun reaches the earth surface, it is:
  transmitted
  absorbed
  reflected
The nature of how the earth materials transmit, absorb or reflect the solar EMR is called spectral signature of an object

## Slide 12: SPECTRA OF EARTH MATERIALS
geografia.science.upjs.sk katarina.onacillova@upjs.sk
Objects/surfaces have different combination of transmittance, absorbtion and reflectance in different bands of the spectrum
INSTITUTE OF GEOGRAPHY, FACULTY OF SCIENCE, PAVOL JOZEF ŠAFÁRIK UNIVERSITY IN KOŠICE, SLOVAKIA

## Slide 13: SPECTRA OF EARTH MATERIALS
1.) Data review:
File - Open Image
- after selecting the file, a window called Set display specifications opens,
which is used to set the visualization parameters of the selected file. In the Channels item, three bands can be selected, which will then be displayed in the form of a color composition (synthesis). It is also possible to edit the image by changing the settings in the Enhancement item.
An example of displaying the false color composition using data from the HS scanner AISA KESTREL and the corresponding RGB bands of the scanner.
False color composition:
e.g. bands 300, 150, 50

## Slide 14: 2.) Display of the spectral curves: Window – New selection graph

## Slide 15: MULTISPEC
II. IMAGE CLASSIFICATION

## Slide 16
UNSUPERVISED CLASSIFICATION
II.I
MultiSpec

## Slide 17
Open image
File - Open Image
Write Cluster Report/Map to
  Cluster mask file
  Image Window Overlay
Choose ussupervised classification
algorithm:
Processor – Cluster – choose algoritm
  ISODATA or Single pass

## Slide 18: 4. Set ISODATA Cluster specifications:
Compared to the Single pass algorithm, you can set the number of clusters (Number clusters) and, similarly to the previous case, the value of the minimum number of pixels forming a cluster (Minimum cluster size). The Convergence (%) parameter affects the number of successive repeated calculations of new cluster centers - iterations. If the number of pixels that do not change their belonging to a certain cluster during the iteration exceeds the specified value, then so-called clusters are created. stable and the calculation is finished.
The method of cluster initialization, which you set in the upper left part of the window (Initialization options), is also important for the classification result. Here you determine how the initial positions of the clusters are to be established in the multidimensional space defined by the individual input bands. The first two options mean that the initial position of the clusters is determined by the principal component analysis method, the third option takes over the result of the single- pass algorithm

## Slide 19: 5. Editing the result of unsupervised classification
The clustering result is a thematic map stored in the *.clu file. In the text window of the Multispec program, you will also see the results of the classification in a clear tabular form. Above all, you will find here the resulting number of clusters and the number of pixels included in each of them. Open the saved classification file using the File – Open Image menu.
With a larger number of clusters and thus resulting spectral classes, the classified image is difficult to interpret. The colors of individual clusters in the image can be changed by double-clicking on the color icon next to the cluster so that they simulate the color presentation of the selected synthesis. This will make it much easier for you to interpret individual classes, recognize them, or eventually combine (aggregate) several spectral classes (clusters) into categories of basic types of surfaces.
Analogously, you change the name of individual classes by double clicking on the text next to the colored square of the legend.

## Slide 20: 6. Repeat the process of unsupervised
classification with „stacked data“ – HS + CHM
HS data LS data – CHM model
+
=

## Slide 21
SUPERVISED CLASSIFICATION
II.II
MultiSpec

## Slide 22: 1. File - Open Image
2. Create training samples (polygons) - Processor – Statistics … Set Project Options.
In this window, check the item Show Train/Test Label and confirm the choice. A new window will open where you can check the Polygon Enter option to start creating a training sample for the corresponding land cover type. After creating a training sample (polygon), it is necessary to add the sample to the list via the Add To List option... Via the "New" Class option, we enter the name of the new class, into which other clicked training samples for the same type of land cover will be gradually included. If we want to add a polygon to an already existing class, from the Class drop-down menu we choose the corresponding, already created class, in which we want to include the sample.

## Slide 23
3. Processor – Classify opens a window called Set Classification Specifications. In this window, you can choose both the qualifier type (Procedure menu) and the selected input parameters of the selected procedure. Leave the default values of the parameters, but check the Disk file box, which will allow you to save the classification results in a new file of the type e.g. GeoTIFF to disk. You can also check the Image Window Overlay option to directly display the classification result in the MultiSpec window. Confirm the Update projectstatistics windowand save the output.
Classifiers that can be used for classification:
Maximum likelihood (maximum likelihood classifier - belongs to the most frequently
used decision rules in controlled classification of satellite images and gives good results with suitable training areas
Correlation (SAM) – classification of the so-called spectral angle, a decision rule originally used for hyperspectral image data...

## Slide 24
4. Evaluation of the result of supervised classification
-In addition to the file with classified data, the output of individual algorithms is also directed to the text window of the Multispec program. This window can be saved as a text file using the menu File - Save text output as...

## Slide 25: III
PCA - Principal Component Analysis
- Creating new variables/components that are a linear combination of the original variables without substantial loss of information
MultiSpec

## Slide 26
1.) Open image
File - Open Image
2. Transform the
image using the method of
principal components by selecting Processor – Utilities – Principal Component Analysis. In the window that opens, you can set parameters that define the range of input data. The analysis can include all or only some of the bands of the hyperspectral image (Subset), the entire range of rows and columns or only a part of them
3. Save eigenvalues/eigenvectors - that are used to calculate the so-called main components – mutually uncorrelated data transformed into a new space. Also check the option to save as text output (Note: do not check the option to save to Disk file!). The transformation matrix can also be saved to a file on disk by selecting File – Save Transformation Matrix. It is saved in the directory where the original data is located as a file with the same name as the original data with the ending *.TRA. The results of all calculations are also displayed in the text window of the program.

## Slide 27
4. Processor – Reformat – Change Image File Format. In the window that appears, check Transform data and in the new window choose New Channels from PC Eigenvectors. You can select only a subset (if you want to use only certain/significant principal components that e.g. comprise more than 3% - you can find them in the text window) or all bands. Confirm the following two requests with the OK button. Subsequently, you are invited to save the image created by the analysisof the main components in a *.LAN file. Enter a file name and save it.

## Slide 28: 5. Next, you can view the transformed image. Choose File - Open Image. Select the resulting file of type *.LAN. In the Set Display Specifications for ... window, select Side by Side Channels as the Display type. This allows you to view the individual main components side by side in the form of grayscale images, as in the images below.
A sample of nine images transformed by the principal component analysis method from the AISA KESTREL bands. Notice the gradual loss of useful information, or noise increase in major components with higher numbers. PCA will therefore allow us to use instead of all bands after transformation for further work, such as to create a color composition, only a subset - the first e.g. three components that capture the largest part of the information, and we can neglect the remaining bands, as they include only a negligible part of the information. This will speed up e.g. subsequent creation of image classification.

## Slide 29: CONCLUSION
The aim of this practical was to demonstrate how quickly and (relatively) precisely we can classify HS data for e.g. estimation of land cover classes
Fusion of HS and lidar data
Spectral information, spatial (geometry) + surface structure (CHM)
Today, we have even more sensitive and precise algorithms for HS data classification that generate even better results, like machine and deep learning, however, they require more time for processing/ and various input data

## Slide 30
THANK YOU
FOR
YOUR ATTENTION
geografia.science.upjs.sk katarina.onacillova@upjs.sk
INSTITUTE OF GEOGRAPHY, FACULTY OF SCIENCE, PAVOL JOZEF ŠAFÁRIK UNIVERSITY IN KOŠICE, SLOVAKIA
Katarína ONAČILLOVÁ, Michal GALLAY, Ján ŠAŠAK
INTERNATIONAL REMOTE SENSING SUMMER SCHOOL , IV EDITION
Experiencing Remote Sensing on Sardinia inland site: Advanced summer school on instruments and methodology for a CAL/VAL site for Optical data SAN VERO MILIS | SARDINIA, italy | 21. - 25. JULY 2025