## Slide 1
INTERNATIONAL REMOTE SENSING SUMMER SCHOOL , IV EDITION
Experiencing Remote Sensing on Sardinia inland site: Advanced summer school on instruments and methodology for a CAL/VAL site for Optical data SAN VERO MILIS | SARDINIA, italy | 21. - 25. JULY 2025
INSTITUTE OF GEOGRAPHY, FACULTY OF SCIENCE, PAVOL JOZEF ŠAFÁRIK UNIVERSITY IN KOŠICE, SLOVAKIA
geografia.science.upjs.sk
Introducing the UAV hyperspectral scanning Michal Gallay, Katarína Onačillová, Ján Šašak

## Slide 2
Imaging spectrometer used for hyperspectral imaging
Can measure thousands or hundreds of thousands of spectra
The collected spectra are used to form an image of the target, thus we get spectrum and location
Data that hyperspectral imaging provides is called a data cube
→ This is huge amount of accurate information
HYPERSPECTRAL CAMERA

## Slide 3
HYPERSPECTRAL CAMERA
WHY data cube?
When HS camera moves relative to target we get our 3rd dimension, which is also location, but in perpendicular direction. This is why it’s called a cube.

## Slide 4
SPECTRAL SIGNATURES
Spectral signatures can be compared to fingerprints
Since every material and compound reacts to light uniquely, their spectral signatures are unique too
Just like fingerprints can be used to identify a person, spectral signatures can be used to identify material
Spectrometer is an instrument that splits incoming light into a spectrum
In the example on the left light going through the spectrometer is reflected, and the result is called a reflectance spectrum

## Slide 5
Hyperspectral imaging combined with UAS:
fast, flexible and non-destructive detection of subtle spectral features
Chance to develop R&D infrastructure via the EU structural funds
UAV Hyperspectral remote sensing
Notes: While the photo cameras or multispectral cameras have been the most popular sensors for mini and small UAV systems, the integrated use of UAV hyperspectral imaging and/or laser scanning is a recent issue, because of reducing the size and weight of hyperspectral scanner allows for their integration on UAV platforms. Hyperspectral remote sensing, also known as imaging spectroscopy, is a relatively new technology for UAV platforms that has been used in detection of vegetation species and biomass (Aasen, H. et al., 2015) or precision agriculture (Zarco-Tejada et al., 2013; Bareth et al., 2015; Sima et al., 2016).
Hyperspectral imaging sensors (spectrometers) capture reflected electromagnetic energy in hundreds of contiguous narrow spectral bands with high spectral resolution, typically in visible and near-infrared spectrum. Such sensors combined with unpiloted aerial systems (UAS) enable fast, flexible and non-destructive detection of subtle spectral features and dynamics of landscape changes.
The power and value of hyperspectral imaging four our team is in its capability to - Identify, Quantify (Measure) and Map landscape properties in each pixel of the target image.

## Slide 6
Our UAV HS system
Push-broom (line) imaging scanner
PUSH-BROOM
Full spectral data simultaneously
Image is recorded per line, for all wavelenghts at the same time
Notes: “Pushbroom” spectrometers use a 2D detector array, and thus collect a vertical slice of the datacube at once so that only one spatial dimension needs to be scanned to fill out the cube.2 A filtered camera, constructed by placing a filter wheel or tunable spectral filter in front of a camera, collects a horizontal slice and thus needs to scan along the spectral dimension to complete the data set.
Pushbroom: Full spectral data simultaneously, with spatial line scanning over time. Imaging spectrograph + 2D array detector
The pushbroom approach, also known as line scanning, has been used by some earth observation satellite systems operating from space, such as the SPOT system. Different from the whiskbroom method that scans one point at a time, the pushbroom method can simultaneously. acquire a slit of spatial information, as well as spectral information corresponding to each spatial point in the slit for one scan, that is, a special y − λ image with one spatial dimension (y) and one spectral dimension (λ) can be taken at the same time with a matrix detector. As shown in Fig. 2(b), the pushbroom method collects a slit image from the object dispersed onto a 2-D detector, in which the spatial information is displayed along one axis and wavelength information along the other. Then the spectral image data cube can be obtained by scanning the slit in the direction of another spatial axis. A pushbroom scanner can get more light than the whiskbroom one, since it can stay at a particular area for a longer time providing a long exposure on the matrix detector and a relatively high spectral resolution as well. However, in most of the pushbroom imagers, either the camera or the object should move accordingly as one line of the image is acquired at each scan and the move should be synchronized with the frame acquisition rate of the array detector in order to ensure the measurement of a smooth image. Another approach to perform the pushbroom procedure is to put a movable slit aperture or a rolling shutter into the conjugate image plane to eliminate out-of-focus light. This method allows for higher illumination transmission while exhibiting only a slight increase in the confocal depth response, which has been widely used in multispectral line confocal imaging systems.

## Slide 7
Our UAV HS system
Push-broom vs other typical spectral imaging approaches
PUSH-BROOM
Full spectral data simultaneously
Image is recorded per line, for all wavelenghts at the same time
Whiskbroom
Pushbroom
Staring
Snapshot
Quingly, L. et al (2013)
Notes: “Pushbroom” spectrometers use a 2D detector array, and thus collect a vertical slice of the datacube at once so that only one spatial dimension needs to be scanned to fill out the cube.2 A filtered camera, constructed by placing a filter wheel or tunable spectral filter in front of a camera, collects a horizontal slice and thus needs to scan along the spectral dimension to complete the data set.
Pushbroom: Full spectral data simultaneously, with spatial line scanning over time. Imaging spectrograph + 2D array detector
The pushbroom approach, also known as line scanning, has been used by some earth observation satellite systems operating from space, such as the SPOT system. Different from the whiskbroom method that scans one point at a time, the pushbroom method can simultaneously. acquire a slit of spatial information, as well as spectral information corresponding to each spatial point in the slit for one scan, that is, a special y − λ image with one spatial dimension (y) and one spectral dimension (λ) can be taken at the same time with a matrix detector. As shown in Fig. 2(b), the pushbroom method collects a slit image from the object dispersed onto a 2-D detector, in which the spatial information is displayed along one axis and wavelength information along the other. Then the spectral image data cube can be obtained by scanning the slit in the direction of another spatial axis. A pushbroom scanner can get more light than the whiskbroom one, since it can stay at a particular area for a longer time providing a long exposure on the matrix detector and a relatively high spectral resolution as well. However, in most of the pushbroom imagers, either the camera or the object should move accordingly as one line of the image is acquired at each scan and the move should be synchronized with the frame acquisition rate of the array detector in order to ensure the measurement of a smooth image. Another approach to perform the pushbroom procedure is to put a movable slit aperture or a rolling shutter into the conjugate image plane to eliminate out-of-focus light. This method allows for higher illumination transmission while exhibiting only a slight increase in the confocal depth response, which has been widely used in multispectral line confocal imaging systems.

## Slide 8
OUR UAV HS SYSTEM
Rectification process
  With a push-broom spectrometer, full spectral image is recorded per line
  However, each line of airborne pushbroom images is collected at different time instants
  perspective geometry varies with each line
  different line displacement
  Rectification process is needed
Notes:   With a push-broom spectrometer, full spectral image data are recorded simultaneously per line
  However, each line of airborne pushbroom images is collected at different time instants. Perspective geometry varies with each pushbroom line, leading to different line displacement, and thus turning the rectification process more difficult

## Slide 9
  Rectification of the raw image data:
  requires measuring position and attitude of the sensor enabled by IMU/GNSS unit on-board the UAV
  Accurate alignment of overlapping data strips requires compensating for geometric distortions caused by boresight misalignment → BORESIGHT CALIBRATION
OUR UAV HS SYSTEM
Boresight calibration of push-broom sensor
Notes:   Rectification of the raw image data requires measuring the position and attitude the sensor which is enabled by IMU/GNSS unit on-board the UAV
  Accurate alignment of overlapping data strips requires compensating for geometric distortions caused by boresight misalignment - boresight calibration

## Slide 10
Hyperspectral payload
AISA Kestrel 10
  Push-broom camera, 4.75 kg
  F/2.4, FOV: 40°
  Spatial resolution: 1024 or 2048 pix.
  Spectral range: 400 – 1000 nm
  Spectral sampling: 1.75/3.5/7 nm
  Max. number of spectral bands: 342
  Radiometric res: 16bit unsigned integer
  Frame rate: <100 Hz
  SNR : 400-800
  Total system power: <41 W
OUR UAV HS SYSTEM

## Slide 11
UAV HYPERSPEctral MISSION
PLANNING
DATA ACQUISITION
DATA PROCESSING
RESULTS

## Slide 12
UAV flight mission: area of interest (AOI)
500 m
2000 m
Stagno di Salede Porcus
Northern part, 500 x 1000 m

## Slide 13
Flight mission parameters: FOV, swath width, spatial resolution
AISA Kestrel 10

## Slide 14
1000 m
Stagno di Salede Porcus
Northern part, 500 x 1000 m
HS camera FOV = 40°
Tan(40°/2) x 90 m flying height = 29,1 m, approx. 58 m swath width
If 1024 pixels per line: 58 : 1024 = 5,6 cm
Number of flight lines given a 450 m width of AOI, E-W direction:
450 m/58 m = 7.75 lines
Account for 20% flight line overlap:
7.75/0.80 = 9.68 so that 10 flight lines
450 m
Frames Per Second : Flight speed/pixel size =
5 m/s / 0.056 m = 89.2 thus 90 FPS
Exposure time 1/FPS: 1/90 = 0.011 s = 11 ms
Flight mission parameters: FOV, swath width, spatial resolution

## Slide 15
Settings of the HS camera before the mission

## Slide 16
Frame rate, given in frame per second (fps) or Hz, defines the pace for your target sampling
In airborne systems this is related to airspeed, or ground speed to be more exact
If your ground speed is 60 m/s you get 1 m sampling on the ground by using 60 fps
Our max. frame rate is 100 Hz, and max flight speed 10 m/s
Thus, with this speed we can sample at 10 cm
Frame rate and frame time

## Slide 17
Frame time is also called frame interval
It is given in milliseconds (ms)
Frame time is inverse of frame rate (1/fps)
It helps you to understand the relationship between frame rate and exposure time
For example:
Frame rate and frame time

## Slide 18
Motion blur occurs when you have relative motion betweenthe sensor and target
The longer the exposure time, more blur there is
It makes the image to look ”softer” and less sharp
To maximise signal you would like to use as long exposure time as possible, but from blur perspective the shorter exposure time would be better. You need to compromise
Be careful of overexposure (more signal than can be recorded) underexposure (low signal and low SNR)
Rule of thumb: To set the suitable frame time, the recorded signal of a white target is at about 75% of capacity (there is some reserved capacity)
Motion blur

## Slide 19
Binning is the procedure of combining the signal from a number of adjacent pixels into an output for a single pixel
Binning can be on-chip (summing) or off-chip (summing or averaging)
In all AISA instruments non-symmetrical (2x1, 2x4, 2x8) binning is preferred
Vertical binning setting defines spectral bandwidth
Horizontal binning controls spatial resolution
Frame rate is independent of binning
SNR improves by up to square root of the binning factor
Spectral and spatial binning of the recorded signal

## Slide 20
There are two primary benefits from binning
Improved SNR, due to less read noise, by up to a factor of binning
Increased frame rate, when vertical (spectral) binning is applied
Horizontal binning reduces spatial resolution
Spectral and spatial binning of the recorded signal

## Slide 21
DSM and ortorectification
Often the ground elevation and height of objects on the ground varies relatively large amounts compared to height
In such a case it’s important to use Digital surface model (DSM) when processing the HS data, because target object size changes
For flat surfaces constant elevation can be used and is sufficient (no DSM)

## Slide 22
Flying with pushbroom sensor is different from 2D image cameras
Try to maintain as well as possible
Constant speed
Constant altitude
Constant heading vs. course ..., not so easy due to wind/UAV tilt
When acquiring data
Do not hover above target/area
Do not turn in-place
Issues to consider for mission planning/flight

## Slide 24: Hyperspectral data acquisition and processing
Stagno di Sal’e Porcus
18-20 July 2023
Michal Gallay, Ján Kaňuk, Ján Šašak, Katarína Onačillová

## Slide 25: Description of UAV HS mission in the northern part of Salle Porcus, Sardegna, IRSS 2023
There were 2 UAV HS missions:
18.7.2023, sunny, grey sky with haze? of high cirrus, over 40°C, between 11-13:00
20.7.2023, sunny, blue sky, no visible cirrus, about 36°C, between 11-14:00
19.7.2023, radiometric targets were spectraly measured in the field, they were put on the surface of the salt lake, ASD FieldSpec, by Massimo from INGV Rome
Sensor: AISA Kestrel 10 by Specim
Above ground flying height: 80 m
Geospatial reference WGS 84 during acquisition,
  after post-processing WSG 84 UTM 32 N
DSM for orthorectification: cell size 50 cm, derived from lidar VUX1 UAV scanning performed on 18/07/2023

## Slide 26: Example of raw data before rectification and georeferencing

## Slide 27: Example of spatial accuracy with respect to orthophoto 2019 SardegnaSentieri.it
  WSG 84 UTM 32 N

## Slide 28: Flight trajectory and image line numbers
Line 1
Line 2
20 July 2023, spectral x spatial binning for data acquisition 2 x 2

## Slide 29: Flight trajectory and image line numbers
Line 3
Line 5, includes radiom. targets
20 July 2023, spectral x spatial binning for data acquisition 2 x 2
Line 4
Line 6

## Slide 30: Flight trajectory and image line numbers
Line 7
Line 8
Line 9
18 July 2023, spectral x spatial binning for data acquisition 4 x 2

## Slide 31: Line 1-6 acquired 20 July and lines 7,8,9 on 18 July 2023 raw data processed in CaligeoPro, a software by Specim
Spectral x spatial
binning during acquisition flight
Line 1 : 2x2 – processed as 8x2
Line 2 : 2x2 – processed as 8x2
Line 3 : 2x2 – processed as 8x2
Line 4 : 2x2 – processed as 8x2
Line 5 : 2x2 – processed as 8x2
Line 6 : 2x2 – processed as 8x2
Line 7 : 4x2 – processed as 8x2
Line 8 : 4x2 – processed as 8x2
Line 9 : 4x2 – processed as 8x2
DN processed as raw data – dark current, then into radiance
Georeferenced AISA data file radiometrically corrected to radiance (mW/cm^2*str*um)*1000.00
1
2
3
4
5
6
7
8
9

## Slide 32: Spectral radiance
(mW/cm^2*str*um)*1000.00
The radiance was produced by:
Subtracting dark current values/signal from raw data
Calibrating the resulting DN to calculate radiance by 8 spectral x 2 spatial binning
Radiance values should be divided by 1000 to get mW/cm^2*str*um
resulting spatial resolution /pixel is 0.1 m
368 spectral bands from 380-1000 nm
Orthorectification was based on a lidar DSM of 0.5 m spatial resolution
This is the output from CALIGEO PRO software and should be used in ENVI for reflectance calculation
Resulting files DAT (image data), HDR (header info), for the image file, OPT (metadata about processing the raw data)

## Slide 33: Empirical line correction to calculate reflectance
Spectral radiance data was used
Based on 5 radiometric targets made of felt
Reflectance of the targets measured in the field 19 July by ASD field spectrometer
This reflectance was used in ELC to calculate reflectance of lines 1-6 from radiance data
Alternatively just the white target could be used for simpler atmos. correction.
Reflectance = (DN/DN white ref) x Reflectance white ref
E.g. Reflectance for DN = 50 = (50/217) x 0.85 = 0.19
Spectralon reference panel

## Slide 34: Radiometric targets in Line 5 with ASD field measured spectral reflectance
Radiance of the radiometric targets, scale factor 1000
ASD field measured reflectance of the radiometric targets
NB: ASD field measured reflectance of white target is higher than 1

## Slide 35: Calibration factors – solar and path radiance calculated based on line 5 radiometric targets
Calibration factors file used to calculate reflectance of line 1,2,3,4,6
Lines 7,8,9 have different spectral and spatial binning during acquisition, therefore, could not be corrected with this ELC methods

## Slide 36: ELC reflectance

## Slide 37: Empirical line correction (ELC)
Lines 7-9 were flown earlier on Tuesday with different spectral binning (4x2) which causes problem in applying ELC based on radiometric targets flow on Thursday at 2x2 binning
FLAASH could be used to derive reflectance
ELC reflectance in the image of line 5 is higher than 1 for the white target, as the field measurement was above 1 for this target.
The supplier of the radiometric targets (a Finish company) measured reflectance of the felt, and it is about 0.2 value lower than measured in the field by ASD spectrometer (compare it for the white target)
these laboratory measurements were not used to date, reflectance is calculated for lines 1-6 based on the ASD reflectance measurements of the targets in the field.
This issue should be tested.
ASD field measured reflectance of the radiometric targets

## Slide 38
Michal gallay, Ján kaňuk, Ján ŠAŠAK, Katarína onačillová
GRAZIE PER ATTENZIONE!
geografia.science.upjs.sk
INSTITUTE OF GEOGRAPHY, FACULTY OF SCIENCE, PAVOL JOZEF ŠAFÁRIK UNIVERSITY IN KOŠICE, SLOVAKIA
INTERNATIONAL REMOTE SENSING SUMMER SCHOOL , IV EDITION
Experiencing Remote Sensing on Sardinia inland site: Advanced summer school on instruments and methodology for a CAL/VAL site for Optical data SAN VERO MILIS | SARDINIA, italy | 21. - 25. JULY 2025