## Slide 1
Airborne Laser Scanning
data quality assessment, lidar data classification, geomorphometric analysis
INTERNATIONAL REMOTE SENSING SUMMER SCHOOL
Experiencing Remote Sensing on Sardinia inland site: Advanced summer school on instruments and methodology for a CAL/VAL site for Optical data
San Vero MiLIS | italy | 17. - 21. july 2023
INSTITUTE OF GEOGRAPHY, FACULTY OF SCIENCE, PAVOL JOZEF ŠAFÁRIK UNIVERSITY IN KOŠICE, SLOVAKIA
Ján kaňuk, Ján ŠAŠAK, Michal gallay, Katarína onačillová
geografia.science.upjs.sk jan.kanuk@upjs.sk

## Slide 2
geografia.science.upjs.sk jan.kanuk@upjs.sk
1st part: LiDAR data quality assessment
flight strip overlaps check
merging of flight strips
statistical infomration about LiDAR data
2nd part: LiDAR data classification
LiDAR data tiling
LiDAR data denoising
ground points extraction
LiDAR data classification
COntent
INSTITUTE OF GEOGRAPHY, FACULTY OF SCIENCE, PAVOL JOZEF ŠAFÁRIK UNIVERSITY IN KOŠICE, SLOVAKIA
3rd part: Geomorphometric analysis
DTM derivation from LiDAR data
derivation of terrain morphometric parameters
raster resampling
Notes: While the photo cameras or multispectral cameras have been the most popular sensors for mini and small UAV systems, the integrated use of UAV hyperspectral imaging and/or laser scanning is a recent issue, because of reducing the size and weight of hyperspectral scanner allows for their integration on UAV platforms. Hyperspectral remote sensing, also known as imaging spectroscopy, is a relatively new technology for UAV platforms that has been used in detection of vegetation species and biomass (Aasen, H. et al., 2015) or precision agriculture (Zarco-Tejada et al., 2013; Bareth et al., 2015; Sima et al., 2016).
Hyperspectral imaging sensors (spectrometers) capture reflected electromagnetic energy in hundreds of contiguous narrow spectral bands with high spectral resolution, typically in visible and near-infrared spectrum. Such sensors combined with unpiloted aerial systems (UAS) enable fast, flexible and non-destructive detection of subtle spectral features and dynamics of landscape changes.
The power and value of hyperspectral imaging four our team is in its capability to - Identify, Quantify (Measure) and Map landscape properties in each pixel of the target image.

## Slide 3
Data & Software
Data
LiDAR point cloud devided to flight strips
Software
LAStools
QGIS
Notes: “Pushbroom” spectrometers use a 2D detector array, and thus collect a vertical slice of the datacube at once so that only one spatial dimension needs to be scanned to fill out the cube.2 A filtered camera, constructed by placing a filter wheel or tunable spectral filter in front of a camera, collects a horizontal slice and thus needs to scan along the spectral dimension to complete the data set.
Pushbroom: Full spectral data simultaneously, with spatial line scanning over time. Imaging spectrograph + 2D array detector
The pushbroom approach, also known as line scanning, has been used by some earth observation satellite systems operating from space, such as the SPOT system. Different from the whiskbroom method that scans one point at a time, the pushbroom method can simultaneously. acquire a slit of spatial information, as well as spectral information corresponding to each spatial point in the slit for one scan, that is, a special y − λ image with one spatial dimension (y) and one spectral dimension (λ) can be taken at the same time with a matrix detector. As shown in Fig. 2(b), the pushbroom method collects a slit image from the object dispersed onto a 2-D detector, in which the spatial information is displayed along one axis and wavelength information along the other. Then the spectral image data cube can be obtained by scanning the slit in the direction of another spatial axis. A pushbroom scanner can get more light than the whiskbroom one, since it can stay at a particular area for a longer time providing a long exposure on the matrix detector and a relatively high spectral resolution as well. However, in most of the pushbroom imagers, either the camera or the object should move accordingly as one line of the image is acquired at each scan and the move should be synchronized with the frame acquisition rate of the array detector in order to ensure the measurement of a smooth image. Another approach to perform the pushbroom procedure is to put a movable slit aperture or a rolling shutter into the conjugate image plane to eliminate out-of-focus light. This method allows for higher illumination transmission while exhibiting only a slight increase in the confocal depth response, which has been widely used in multispectral line confocal imaging systems.

## Slide 4
LiDAR data quality assessment
Tool: lasoverlap
  the tool checks the flight line overlap and the vertical and horizontal alignment
  Parameters: pixel/step size 0.5 m
  subsample 1
  min diff value 0
  max diff value 0.5
Notes:   With a push-broom spectrometer, full spectral image data are recorded simultaneously per line
  However, each line of airborne pushbroom images is collected at different time instants. Perspective geometry varies with each pushbroom line, leading to different line displacement, and thus turning the rectification process more difficult

## Slide 5
LiDAR data quality assessment
Tool: lasmerge
  the tool merges several flight lines into one point cloud
  the output point cloud is saved in the „bin“ folder
Notes:   With a push-broom spectrometer, full spectral image data are recorded simultaneously per line
  However, each line of airborne pushbroom images is collected at different time instants. Perspective geometry varies with each pushbroom line, leading to different line displacement, and thus turning the rectification process more difficult

## Slide 6
LiDAR data quality assessment
Tool: lasinfo
  the tool merges several flight lines into one point cloud
  UAV lidar data
  national airborne lidar data
Notes:   With a push-broom spectrometer, full spectral image data are recorded simultaneously per line
  However, each line of airborne pushbroom images is collected at different time instants. Perspective geometry varies with each pushbroom line, leading to different line displacement, and thus turning the rectification process more difficult

## Slide 7
LiDAR data Classification
Tool: lasclip
  the tool clips point cloud againts polygonal layer
polygon
Notes:   With a push-broom spectrometer, full spectral image data are recorded simultaneously per line
  However, each line of airborne pushbroom images is collected at different time instants. Perspective geometry varies with each pushbroom line, leading to different line displacement, and thus turning the rectification process more difficult

## Slide 8
LiDAR data Classification
Tool: lasindex
  the tool creates LAX file that contains spatial indexing information
Tool: lastile
  the tool tiles point cloud into regular square tiles
  Parameters: tile size 50 m
  buffer 5 m
  ll_x (shift along the X axis) 57 m
  ll_y (shift along the Y axis) 30 m
Notes:   With a push-broom spectrometer, full spectral image data are recorded simultaneously per line
  However, each line of airborne pushbroom images is collected at different time instants. Perspective geometry varies with each pushbroom line, leading to different line displacement, and thus turning the rectification process more difficult

## Slide 9
LiDAR data Classification
Tool: lasnoise
  removes or flags isolated (noise) points from point cloud
NOISE
Notes:   With a push-broom spectrometer, full spectral image data are recorded simultaneously per line
  However, each line of airborne pushbroom images is collected at different time instants. Perspective geometry varies with each pushbroom line, leading to different line displacement, and thus turning the rectification process more difficult

## Slide 10
LiDAR data Classification
Tool: lasground
  extracts ground points from point cloud and splits the points into two categories – ground and unclassified points
ground points
unclassified points
  Parameters: landscape type - wilderness
  ignore points – low noise (7) and high noise (18)
  tick the option „compute height“
Notes:   With a push-broom spectrometer, full spectral image data are recorded simultaneously per line
  However, each line of airborne pushbroom images is collected at different time instants. Perspective geometry varies with each pushbroom line, leading to different line displacement, and thus turning the rectification process more difficult

## Slide 11
LiDAR data Classification
Tool: lasclassify
  classifies unclassified points to buildings and vegetation categories
ground points
unclassified points
vegetation
Notes:   With a push-broom spectrometer, full spectral image data are recorded simultaneously per line
  However, each line of airborne pushbroom images is collected at different time instants. Perspective geometry varies with each pushbroom line, leading to different line displacement, and thus turning the rectification process more difficult

## Slide 12
LiDAR data Classification
Tool: las2las
  exports ground points from classified point cloud
  Parameters: filter by classification or return – keep_classification – number or value „2“
Notes:   With a push-broom spectrometer, full spectral image data are recorded simultaneously per line
  However, each line of airborne pushbroom images is collected at different time instants. Perspective geometry varies with each pushbroom line, leading to different line displacement, and thus turning the rectification process more difficult

## Slide 13
GEOmorphometric analysis
Tool: blas2dem
  creates raster models of elevation, intensity, slope or RGB
  Parameters: step 0.1 m; item - elevation
Notes:   With a push-broom spectrometer, full spectral image data are recorded simultaneously per line
  However, each line of airborne pushbroom images is collected at different time instants. Perspective geometry varies with each pushbroom line, leading to different line displacement, and thus turning the rectification process more difficult

## Slide 14
GEOmorphometric analysis
Software: QGIS
  data import: Drag & Drop/Layer - Add Layer - Add Raster Layer
Notes:   With a push-broom spectrometer, full spectral image data are recorded simultaneously per line
  However, each line of airborne pushbroom images is collected at different time instants. Perspective geometry varies with each pushbroom line, leading to different line displacement, and thus turning the rectification process more difficult

## Slide 15
GEOmorphometric analysis
Software: QGIS
  geomorphometric analysis: Processing - Toolbox - Raster Terrain Analysis - Slope/Aspect
  Slope
  Aspect
Notes:   With a push-broom spectrometer, full spectral image data are recorded simultaneously per line
  However, each line of airborne pushbroom images is collected at different time instants. Perspective geometry varies with each pushbroom line, leading to different line displacement, and thus turning the rectification process more difficult

## Slide 16
THANK YOU FOR YOUR ATTENTION
geografia.science.upjs.sk jan.kanuk@upjs.sk
INSTITUTE OF GEOGRAPHY, FACULTY OF SCIENCE, PAVOL JOZEF ŠAFÁRIK UNIVERSITY IN KOŠICE, SLOVAKIA
Ján kaňuk, Ján ŠAŠAK, Michal gallay, Katarína onačillová
INTERNATIONAL REMOTE SENSING SUMMER SCHOOL
Experiencing Remote Sensing on Sardinia inland site: Advanced summer school on instruments and methodology for a CAL/VAL site for Optical data
San Vero MiLIS | italy | 17. - 21. july 2023