## Slide 1
Facing Cal/Val and Surface Classification by Using Multi Instrument Approach
Massimo Musacchio 1, Malvina Silvestri1, Federico Rabuffi1, Marco Casu3 Ilaria Nobile3 Maria Titi Melis3 Marco Solinas1, Michal Gallay3, Ján Šašak3 , Katarína Onačillová3 , Petra Dávidová3
Challenge
In the context of the global transition to a green economy and the growing demand for energy security, hyperspectral remote sensing assumes as a key technology for mineral and hydrocarbon exploration. To accomplish this, orbital hyperspectral imaging (HSI) systems require high radiometric and spectral accuracy, which depends on well-characterized ground calibration and validation (Cal/Val) sites. Such sites must exhibit spectral homogeneity and temporal stability to enable robust assessment of sensor performance across multiple spatial and spectral scales.
Multi-scale and multi-instrument approach integrating ground data and laboratory analysis of the Sal 'e Porcus pond (SPp) in Sardinia, Italy, evaluating its suitability as a CAL/VAL reference site for current and upcoming mission.
Approach
Field and Laboratory spectroscopy
X-Ray Diffraction
Remote sensing data
Airborne HyTES
Drone Hyperspectral + LiDAR
Spaceborne PRISMA
Main Characteristics
Largest dry pond in Sardinia - flat-bottomed interdunal depression collecting rainwater. Avg. depth: ~40 cm Max. depth: ~1 m. Hydrologically isolated basin - no tributaries or emissaries.
Seasonal Dynamics: intense evaporation in summer – dry pond - salt-covered surface
Geological and Hydrological Features: Basin bottom composed of greyish-white clay sediments (impermeable). Limited water infiltration enhances surface salt accumulation after evaporation
Relevance: Natural environment for studying evaporitic processes, seasonal salt deposition, surface composition variability, spectral response in saline environments.
By providing a well-documented natural target with known spectral and mineralogical properties, this work supports the calibration and validation of hyperspectral data products. The characterization of Sal 'e Porcus directly contributes to Cal/Val efforts for the PRISMA and follow-on mission (PRISMA-SG) and CHIME in the VSWIR domain, while also providing a reference framework for future thermal infrared missions. This ensure these systems achieve the calibration accuracy needed to resolve spectral features critical for surface mineral mapping
Conclusion
HyTES emissivity R: 10.7 µm, G: 9.2 µm, B: 8.5 µm
HyTES LST
PRISMA - Reflectance
R: 2010.66 nm, G: 1765.51 nm, B: 1273.49 µm
1 Istituto Nazionale di Geofisica e Vulcanologia, Italy 2 University of Cagliari, Italy 3 Institute of Geography, Pavol Jozef Šafárik University, Košice, Slovakia